## Slide 1
Different ways to
speed up computer systems
Keivan Navi
Winter 2025

## Slide 2
knavi@cpp.edu
Outline
Keivan Navi
Pipeline
Super-Pipeline
Super-Scalar
1/30

## Slide 3
General Performance Metrics
Keivan Navi
Performance can be determined by:
  Instruction Count
  Clock Rate
  CPI (Clocks Per Instructions)
Execution Time = Instruction Count * CPI * Cycle Time
The Instruction Count is governed by Compiler’s Techniques and Architectural decisions.
The CPI is primarily governed by Architectural decisions.
The Cycle Time is governed by technology improvements and Architectural decisions.
2/30
knavi@cpp.edu

## Slide 4
Unpipelined Processor
Keivan Navi
Only ONE instruction can be resident at the processor at any given time.
The whole processor is considered as ONE stage, k=1. CPI = 1 / IPC
One Instruction
resident in Processor
The number of stages
,
K
=
1
3/30
knavi@cpp.edu

## Slide 5
Keivan Navi
First method: Pipelining
4/30
knavi@cpp.edu

## Slide 6
Keivan Navi
Pipelining is a key implementation technique used to build fast processors.
It allows the execution of multiple instructions to overlap in time.
The throughput of an instruction pipeline is the measure of how often an instruction exits the pipeline.
So :
Pipelining is a way of speeding up execution of instructions by overlapping the execution of multiple instructions.
Pipelining
5/30
knavi@cpp.edu

## Slide 7
Pipelining
Keivan Navi
Pipelining increases throughput, but not latency.
Limitations:
Computations must be divisible into stage size
Pipeline registers add overhead
6/30
knavi@cpp.edu

## Slide 8
Pipelining Processors
Keivan Navi
Two possible implementations of the MIPS architecture:
  Single-cycle datapath (It executes each instruction in just one clock cycle, but the cycle time may be very long.)
  Multicycle datapath (It has much shorter cycle times, but each instruction requires many cycles to be executed.)
Pipelining gives the best of both worlds and is used in almost every modern processor.
  Cycle times are short so clock rates are high.
  But we can still execute an instruction in about one clockcycle!
Single Cycle Datapath | CPI = 1 | Long Cycle Time
Multi-cycle Datapath | CPI = ~4 | Short Cycle Time
Pipelined Datapath | CPI = ~1 | Short Cycle Time
7/30
knavi@cpp.edu

## Slide 9
Pipelining Processors
Keivan Navi
Executing a MIPS instruction can take up to five steps:
However not all instructions need all five steps.
Step | Name | Description
Instruction Fetch | IF | Read an instruction from memory.
Instruction Decode | ID | Read source registers and generate control signals.
Execute | EX | Compute an R-type result or a branch outcome.
Memory | MEM | Read or write the data memory.
Writeback | WB | Store a result in the destination register.
Instruction | Steps required |  |  |  | 
beq | IF | ID | EX |  | 
R-type | IF | ID | EX |  | WB
sw | IF | ID | EX | MEM | 
lw | IF | ID | EX | MEM | WB
8/30
knavi@cpp.edu

## Slide 10: Types of Instructions
There are 3 different types of instructions:
1- Register Type (R-Type):
2-Laod Store:
3-Branch:
8.5/30

## Slide 11
Single-cycle datapath diagram
Keivan Navi
4
Shift
left 2
PC
Add
Add
0
M
u
x
1
PCSrc
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Read
address
Instruction
memory
Instruction
[31-0]
I [31 - 0]
I [9 - 5]
I [4 - 0]
I [20 - 16]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
9/30
knavi@cpp.edu
How long does it take to execute each instruction?
Write
register

## Slide 12
Pipelining
Keivan Navi
10/30
We shouldn’t have to wait for the entire instruction to complete before we can reuse the functional units. For example, the instruction memory is free in the Instruction Decode step as shown below, so...
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [31 - 0]
I [9 - 5]
I [4 - 0]
I [20 - 16]
0
M
u
x
1
RegDst
Read
register 1
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Instruction Decode (ID)
Idle
knavi@cpp.edu
Read
register 2

## Slide 13
Decoding and fetching together
Keivan Navi
Why don’t we go ahead and fetch the next instruction while we’re decoding the first one?
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [31 - 0]
I [9 - 5]
I [4 - 0]
I [20 - 16]
0
M
u
x
1
RegDst
Read
register 1
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Read
address
Decode 1st instruction
Fetch 2nd
11/30
knavi@cpp.edu
Read
register 2

## Slide 14
Executing, decoding and fetching
Keivan Navi
Similarly, once the first instruction enters its Execute stage, we can go ahead and decode the second instruction. But now the instruction memory is free again, so we can fetch the third instruction!
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [31 - 0]
I [9 - 5]
I [4 - 0]
I [20 - 16]
0
M
u
x
1
RegDst
Read
register 1
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Decode 2nd
Fetch 3rd
Execute 1st
12/30
knavi@cpp.edu
Read
register 2

## Slide 15
Making Pipelining Work
Keivan Navi
We’ll make our pipeline 5 stages long, to handle load instructions as they were handled in the multi-cycle implementation.
  Stages are: IF, ID, EX, MEM, and WB
We want to support executing 5 instructions simultaneously: one in each stage.
13/30
knavi@cpp.edu

## Slide 16
Pipeline terminology
Keivan Navi
filling
full
emptying
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
lw $t0, 4($sp) | IF | ID | EX | MEM | WB |  |  |  | 
sub $v0, $a0, $a1 |  | IF | ID | EX | MEM | WB |  |  | 
and $t1, $t2, $t3 |  |  | IF | ID | EX | MEM | WB |  | 
or $s0, $s1, $s2 |  |  |  | IF | ID | EX | MEM | WB | 
add $sp, $sp, -4 |  |  |  |  | IF | ID | EX | MEM | WB
The pipeline depth is the number of stages—in this case, five.
In the first four cycles here, the pipeline is filling, since there are unused functional units.
In cycle 5, the pipeline is full. Five instructions are being executed simultaneously, so all hardware units are in use.
In cycles 6-9, the pipeline is emptying.
14/30
knavi@cpp.edu

## Slide 17
Pipeline terminology
Keivan Navi
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
lw $t0, 4($sp) | IF | ID | EX | MEM | WB |  |  |  | 
lw $t1, 8($sp) |  | IF | ID | EX | MEM | WB |  |  | 
lw $t2, 12($sp) |  |  | IF | ID | EX | MEM | WB |  | 
lw $t3, 16($sp) |  |  |  | IF | ID | EX | MEM | WB | 
lw $t4, 20($sp) |  |  |  |  | IF | ID | EX | MEM | WB
filling
Execution time on ideal pipeline:
  time to fill the pipeline + one cycle per instruction
  What is the execution time for N instructions?
Compare with other implementations:
  Single Cycle: (8ns clock period)
How much faster is pipelining for N=1000 ?
15/30
knavi@cpp.edu

## Slide 18
Important Observation
Keivan Navi
Each functional unit can only be used once per instruction.
Each functional unit must be used at the same stage for all instructions. See the problem if:
  Load uses Register File’s Write Port during its 5th stage
  R-type uses Register File’s Write Port during its 4th stage
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add $sp, $sp, -4 | IF | ID | EX | WB |  |  |  |  | 
sub $v0, $a0, $a1 |  | IF | ID | EX | WB |  |  |  | 
lw $t0, 4($sp) |  |  | IF | ID | EX | MEM | WB |  | 
or $s0, $s1, $s2 |  |  |  | IF | ID | EX | WB |  | 
lw $t1, 8($sp) |  |  |  |  | IF | ID | EX | MEM | WB
16/30
knavi@cpp.edu

## Slide 19
A solution: Insert NOP stages
Keivan Navi
Enforce uniformity
  Make all instructions take 5 cycles.
  Make them have the same stages, in the same order
    Some stages will do nothing for some instructions
    Stores and Branches have NOP stages too…
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add $sp, $sp, -4 | IF | ID | EX | NOP | WB |  |  |  | 
sub $v0, $a0, $a1 |  | IF | ID | EX | NOP | WB |  |  | 
lw $t0, 4($sp) |  |  | IF | ID | EX | MEM | WB |  | 
or $s0, $s1, $s2 |  |  |  | IF | ID | EX | NOP | WB | 
lw $t1, 8($sp) |  |  |  |  | IF | ID | EX | MEM | WB
R-type | IF | ID | EX | NOP | WB
store | IF | ID | EX | MEM | NOP
branch | IF | ID | EX | NOP | NOP
17/30
knavi@cpp.edu

## Slide 20
Therefore…
Keivan Navi
K –number of pipe stages, instructions are resident at the processor at any given time.
In our example, K=5 stages, number of parallelism (concurrent instruction in the processor) is also equal to 5.
One instruction will be accomplished each clock cycle, CPI = IPC = 1
18/30
knavi@cpp.edu

## Slide 21
Example of a Six-Stage Pipelined Processor
Keivan Navi
19/30
knavi@cpp.edu

## Slide 22
Pipelining & Performance
Keivan Navi
The Pipeline Depth is the number of stages implemented in the processor, it is an architectural decision, also it is directly related to the technology. In the previous example K=5.
The Stall’s CPI are directly related to the code’s instructions and the density of existing dependences and branches.
Ideally the CPI is ONE.
20/30
knavi@cpp.edu

## Slide 23
Keivan Navi
Second method: Super-Pipelining
21/30
knavi@cpp.edu

## Slide 24
Super-Pipelining Processor
Keivan Navi
IF (Instruction Fetch) : requires a cache access in order to get the next instruction to be delivered to the pipeline.
ID (Instruction Decode) : requires the control unit to decode the instruction to identifying what it does.
Obviously the fetch stage cache access requires much more time than the decode stage –combinational logic.
We can subdivide each pipe-stage into m other stages of smaller amount of time required for each stage: minor cycle time.
22/30
knavi@cpp.edu

## Slide 25
Super-Pipelining Processor
Keivan Navi
The machine can issue a new instruction every minor cycle.
Parallelism = K * m.
For this figure: Parallelism = K * m = 4 * 3 = 12
Super-pipelined machine of Degree m=3
23/30
knavi@cpp.edu

## Slide 26
Stage Quantization
Keivan Navi
(a)four-stage instruction pipeline, (b)eleven-stage instruction pipeline
24/30
knavi@cpp.edu

## Slide 27
Keivan Navi
Third method: Superscaling
25/30
knavi@cpp.edu

## Slide 28
Characteristics of Superscalar Machines
Keivan Navi
Simultaneously advance multiple instructions through the pipeline stages.
Multiple functional units => higher instruction execution throughput.
Able to execute instructions in an order different from that specified by the original program.
Out of program order execution allows more parallel processing of instructions.
26/30
knavi@cpp.edu

## Slide 29
Superpipelined Superscalar Machine
Keivan Navi
The superscalar degree is determined by the issue parallelism n, the sub-stages m and the number of stages k.
Parallelism = K * m * n
For this figure: Parallelism = K * m * n = 5 * 3 * 3 = 45
27/30
knavi@cpp.edu

## Slide 30
Deeper Pipeline, a Solution?
Keivan Navi
As mentioned before, the performance is proportional to Instruction Count, Clock Rate and IPC.
Deeper pipeline has fewer logic gate levels in each stage, this leads to a shorter cycle time and higher clock rate.
But deeper pipeline can potentially cause higher penalties for dealing with inter-instruction dependences.
28/30
knavi@cpp.edu

## Slide 31
Bounded Pipelines Performance
Keivan Navi
Scalar pipeline can only initiate at most one instruction every cycle, hence IPC is fundamentally bounded by ONE.
To get more instruction throughput, we must initiate more than one instruction every machine cycle.
Hence, having more than one instruction resident in each pipeline stage is necessary: parallel pipeline.
29/30
knavi@cpp.edu

## Slide 32
From Scalar to Superscalar Pipelines
Keivan Navi
Superscalar pipelines are parallel pipelines: able to initiate the processing of multiple instructions in every machine cycle.
Superscalars are diversified; they employ multiple and heterogeneous functional units in their execution stages.
They are implemented as dynamic pipelines in order to achieve the best possible performance without requiring reordering of instructions by the compiler.
30/30
knavi@cpp.edu

## Slide 33: Acknowledgement
I would like to thank my dear PhD student Samaneh Firouzi for her help, enthusiasm and support for designing this power point.